## Slide 1
Simulation Study of a STATCOM for Reactive Power and Harmonics Compensation

## Slide 2: Challenges for Modern Electricity Grids
Main challenge:
Modern electricity grids are becoming congested due to new types of loads and growing populations.
Increased Power Demand:
Residential and Commercial Electricity Use
Electric Vehicles
Smart Devices and Appliances
Integration of Renewable Energy:
Distributed Energy Resources
Bidirectional Flow
Industrial and Technological Development:
Data Centers
High-Power Industrial Equipment

## Slide 3: One possible Solution: increase the amount of real power from grid
STATCOM can do!

## Slide 4: What is the function of STATCOM?
STATCOM can supply or absorb reactive power into or from the power grid

## Slide 5: What is the function of STATCOM?
STATCOM can increase the power factor of the grid to 1

## Slide 6
Three phase inverter
STATCOM with linear load
STATCOM with non-linear load
What is the process of the whole project?
Stretch goal:

## Slide 7
Function:
Convert DC current into three phase AC current.
Three-phase inverter
Two-level converter:
Power Switches Three half bridges, each phase uses two switches that connect to the positive and negative of the DC supply.
Operation: By switching quickly in a controlled sequence, the inverter generates a stepped waveform that approximates an AC waveform.
PWM: The PWM controls the duty cycle of the switch to generate an AC output voltage that approximates the sine wave.

## Slide 8
Three-phase inverter
Voltage controller and current controller:
Laplace transform
Block diagram
Deriving transfer function

## Slide 9
Three-phase inverter
Verification:
Transfer function verification in MATLAB
Current controller verification
Voltage controller verification
Ripple verification
Deliverables
Current controller
Voltage controller
The three phase inverter

## Slide 10
Switch - The key to verification
Current controller in each phase:

## Slide 11
STATCOM with linear load

## Slide 12: STATCOM with linear load
Reactive power compensation algorithms:
P-Q theory
Clark transform
(Clark transform)
(inverse Clark transform)

## Slide 13: STATCOM with linear load
Deliverables:
Model the STATCOM as an ideal voltage source.
Fully controlled 3 phase STATCOM with linear load
Verification:
Reactive power compensation verification
Current controller verification
Voltage controller verification
Algorithm:

## Slide 14: Modelling the STATCOM as an ideal voltage source

## Slide 15: Fully controlled 3 phase STATCOM with linear load

## Slide 16
Switch - The key to verification

## Slide 17
Stretch goal: STATCOM with non-linear load

## Slide 18: Stretch goal: STATCOM with non-linear load
Characteristics of nonlinear loads：
The voltage is not proportional to the current.
Harmonic currents

## Slide 19
Deliverables
Fully controlled 3 phase STATCOM with non-linear load.
Stretch goal: STATCOM with non-linear load
Verification:
5-order Butterworth low pass filter verification
Current controller verification
Voltage controller verification
Reactive power compensation verification
Harmonics compensation verification

## Slide 20
Fully controlled 3 phase STATCOM with non-linear load

## Slide 21
Switch - The key to verification

## Slide 22
Stretch goal: STATCOM with non-linear load
Harmonics compensation verification
(Before STATCOM is connected)
(After STATCOM is connected)

## Slide 23
Thank you!